## Slide 1
EE450: High Voltage Engineering
Lecture 1

## Slide 2: Outline
Fundamentals of High Voltage Engineering
History of high voltages
Insulating materials
Voltage stresses
Need for high voltages
Testing voltages
High voltage engineering
Levels of high voltages
Applications of high voltage engineering

## Slide 3: History of High Voltages
A high-voltage power system consists of a complex configuration of generators, long- distance transmission lines and localized distribution networks.
Figure 1: Typical power system

## Slide 4: History of High Voltages
The first public power station was put into service in 1882 in London.
  To produce direct current at low voltage
  Its service was limited to highly localized areas
  Used mainly for electric lighting
With the advent of the transformer, DC systems were quickly replaced by AC systems.
T he first major AC power station was commissioned in 1890 at Deptford.
  To produce alternative current at high voltage of 10 kV
  To supply power over a distance of 28 miles
However, in recent years high-voltage direct current (HVDC) transmission has regained some of its earlier popularity.

## Slide 5: History of High Voltages
Advantages of HVDC:
  HVDC provides an economic solution for interconnecting asynchronous AC systems (back-to-back installation)
  HVDC permits a higher power density as compared to AC transmission
Disadvantages of HVDC:
  Excessive station costs
  Voltage transformation is not possible
Consequently, there is a critical distance (600 km - 800 km) at which DC transmission becomes more economical to adopt than AC.

## Slide 6: History of High Voltages
Power transfer capability P of a bipolar DC system is approximately given by,
P = 2 Ud Id
where
Ud is the operating voltage of one line
Id is the current flowing through the line.
Table 1: Power transfer capability of a DC system and its relationships with operating voltage

## Slide 7: History of High Voltages
Power transfer capability P of an AC system is approximately given by,
where
U is the operating voltage.
Z is the wave impedance of a transmission line
Table 2: Power transfer capability of an AC system and its relationships with operating voltage and transfer distance

## Slide 8: History of High Voltages
Over the last hundred years, the demand of electricity has drastically increased. To
meet the load demand, it is desirable to add more generation into the system.
This implies that the transmission lines need to carry bulk power over long distances.
Accordingly, the system voltage levels have steadily increased over the years to deliver more power.
For the same power, an increase in the voltage level results in:
  Lower cost of conductor
  Higher transmission efficiency
It is desirable to increase the transmission voltage, but this causes increased stresses on the insulation.

## Slide 9: History of High Voltages
Figure 1: Major DC systems in chronological order of their installations

## Slide 10: History of High Voltages
2008 1000 kV Jindongnan-Nanyang-Jingmin (China)
Figure 2: Major AC systems in chronological order of their installations

## Slide 11: Insulating Materials
There are two major components in power systems:
  Conductors that conduct electricity such as overhead lines, distribution lines, wires, cables, windings of machines etc.
  Insulators that block the flow of current between live part and ground such as air in overhead lines, paper insulation applied over conductors of generators and transformers, SF6 and vacuum in circuit breakers.
For the reliable operation of power system, we need proper insulation in the power system so that the current must be confined to flow through its intended path.

## Slide 12: Insulating Materials

## Slide 13: Insulating Materials
Therefore, a good understanding of insulation systems is essential to understand:
– Dielectric properties of the insulating materials
−
Physical phenomenon that leads to degradation and failure of insulating materials
– Diagnostic techniques required for evaluating and testing different insulating materials
High voltage engineering deals with the knowledge of the behaviour of dielectrics- insulating materials when subjected to high voltages.

## Slide 14: Insulating Materials
Insulation materials are classified as: solids, liquids, gases and vacuum.
Solid dielectrics: most widely used are XLPE, PVC, ceramic, glass, rubber, resins, reinforced plastics, polypropylene, impregnated paper, wood, cotton, mica, pressboards, bakelite, perspex, ebonite, Teflon etc.
Liquid dielectrics: Petroleum oils are the most common insulating liquids. However, askarels, fluorocarbons, silicones, and organic esters including castor oil are used in high voltage equipment.
Gaseous dielectrics: Atmospheric air is the cheapest and most widely used dielectric. Other gaseous dielectrics are compressed gas at high pressure than atmospheric in power systems such as nitrogen, SF6, and its mixture with CO2 and N2.

## Slide 15: Insulating Materials
Vacuum: If the pressure inside a chamber is maintained below 10-4 torr, it may be considered as vacuum and provides excellent electrical insulation. Ideally, vacuum is the best insulator with field strengths up to 107 V/cm.

## Slide 16: Voltage Stresses
Normal operating voltage
  Operating voltage determines the dimensions of the insulation which forms part of electrical equipment.
  Normal operating voltage does not severely stress the power system’s insulation. Only in special circumstances, for example under pollution conditions, may operating voltages cause problems to external insulation.

## Slide 17: Voltage Stresses
Power systems are subjected to disturbances caused by;
Temporary (or sustained) overvoltages → ground ferroresonance etc.
Switching overvoltages → switching operations
Lightning overvoltages → lightning strikes
faults, load rejection, or
Transient overvoltages can reach up to 6 per unit (1 per unit = nominal voltage).

## Slide 18: Voltage Stresses

## Slide 19: Voltage Stresses
Page 19
No. Type of Overvoltage
Shape Designation
Amplitude Range
Frequency Range
Causes
1.
Temporary overvoltages
Low- frequency oscillations
1.25 – 1.5 pu
0.1 Hz – 3 kHz
2.
Switching overvoltages
Slow front surges
2– 3 pu
50/60 Hz – 20
kHz
3.
2.5 – 4 pu
4.
Lightning overvoltages
Restrike overvoltages, GIS
Fast front surges
Very fast front surges
10 kHz – 3
MHz
100 kHz – 50
MHz
Ground faults Load rejection Ferranti effect Ferro-resonance
Fault interruption De-energization of capacitor banks Energization of lines Energization/de- energization of transformers
Lightning—cloud-to- ground flashes
Opening or closing of circuit breakers,
disconnecting switch
and earthing switch etc.

## Slide 20: Voltage Stresses
Lightning strike to an UHV line
Page 20

## Slide 21: Voltage Stresses
500 kV disconnector opened under load
Page 21

## Slide 22: Voltage Stresses
Short-circuit on 110 kV power line
Page 22

## Slide 23: Need for High Voltages
For the reliable operation of power system, equipment must be designed and tested at very high voltages.
It is necessary to test HV equipment during its development stage and prior to commissioning.
The magnitude and type of test voltage varies with the rated voltage of a particular apparatus.
Basic classification of testing voltages:
  Testing with power frequency and low-frequency AC voltages
  Testing with DC voltages
  Testing with lightning impulse voltages
  Testing with switching impulse voltages
Page 23

## Slide 24: Testing Voltages
Temporary Overvoltages
Switching Overvoltages
Lightning Overvoltages
Very-fast Front Overvoltages
Page 24

## Slide 25: High Voltage Engineering
High Voltage engineering consists of generation, measurement, and control of high voltages, dielectric discharges and electrical insulation breakdown, overvoltages and their protection, and electrical insulation condition monitoring and diagnosis, et al.
Overvoltages and insulation coordination in power systems
Dielectrics and electrical insulation
High voltage testing techniques
Page 25

## Slide 26: High Voltage Engineering
Reliable insulation is related to the application of high voltage systems. Electrical insulation is the physical basis of high voltage engineering.
High voltage tests ensure high voltage system to be operated safely.
HV generation? HV measurement? HV testing
Overvoltages may have much greater magnitudes than normal operating voltages. They do severely stress the insulation of power system.
Insulation
HV testing techniques
Overvoltages
Page 26

## Slide 27: Levels of High Voltage
Definition of High Voltage
  IEC and its national counterparts (IET, IEEE, VDE, etc.) define high voltage
circuits as those with more than 1000 V for AC and at least 1500 V for DC.
  In electric power transmission engineering, high voltage is usually considered any voltage over approximately 35 kV.
  DC systems:
HVDC levels: 600 kV and below UHVDC levels: above 600 kV
Page 27

## Slide 28: Levels of High Voltage
Table: Voltage Classification for HVAC systems
Voltage Class
Page 28
Voltage Range
Low voltage (LV)
V ≤ 1 kV
Medium voltage (MV)
1 kV < V ≤ 66 kV
High voltage (HV)
66 kV < V ≤ 220 kV
Extra high voltage (EHV)
220 kV < V ≤ 800 kV
Ultra high voltage (UHV)
V > 800 kV

## Slide 29: Applications of High Voltage Engineering
Windings of a 220-kV transformer
Page 29

## Slide 30: Applications of High Voltage Engineering
750-kV transmission line
Page 30

## Slide 31: Applications of High Voltage Engineering
Mineral oil in transformer
Page 31

## Slide 32: Applications of High Voltage Engineering
AC testing transformer (left) and DC voltage generator (right)
Page 32

## Slide 33: Applications of High Voltage Engineering
Impulse voltage generator
Page 33

## Slide 34
Page 34